# MISCOM8028G-4GF-8GC-16GT

# 28-Port Full Gigabit Industrial Ethernet Switch

# Product description

MISCOM8028G layer 3 full Gigabit Industrial Ethernet Switch is a high-performance Ethernet communication product specially developed by Maiwe for industrial communication. It supports 8 Gigabit Combo ports + 4 Gigabit Fx ports + 16 Gigabit Tx ports interface configurations. MISCOM8028G is a 19-inch rack-mounted installation that supports front panel installation and rear panel installation.

Features:

- 8x Gigabit combo port+4xGigabit fiber ports +16x10/100/1000M copper ports

- Support RIP/OSPF/PIM Layer 3 Routing Protocol

- Support MW-Ring/MSTP/VRRP/EAPS for network redundancy

- Support multiple management methods and network centralized management

- Single rib type fanless design

- Front and rear indicator design

- IEC61850-3 certified，State Grid Class A standard

# Product specification

| Software performance |
| --- |
| Switch Function | Support VLAN Support GVRP Support port aggregation. Support flow control. Support Rate limit Support broadcast storm suppression. |
| Redundancy protocol | Support VRRP/EAPS Support MW-Ring and the recovery time<20 ms. Support RSTP/MSTP and compatible with STP |
| Multicast technology | Support IGMP snooping/ IGMP v1/v2/v3 Support GMRP Support static multicast. |
| Unicast Routing | Support RIPv1/v2/RIPng/OSPFv1/v2 Support Static Routing Support PIM-SM/PIM-DM |
| Service quality management | Support ACL and L2-L7 data Filter Support SP/ WRR queuing |
| IP management | Support DHCP server/relay/client |
| Management and maintenance | Support Console/Telnet/and Web management methods Support SNMPv1/v2c Support FTP/TFTP file transfer and software update Support power failure alarm/power alarm/ port link down alarm/ring alarm Support port mirroring/Syslog/ LLDP/ RTC/SNTPv4 |
| Technical specifications |
| Ethernet Standard | IEEE802.3-10BaseT IEEE802.3u-100BaseTX/100Base-FX IEEE802.3x-Flow Control, IEEE802.3z-1000BaseLX IEEE802.3ab-1000BaseTX IEEE802.1ab IEEE802.1D-Spanning Tree Protocol IEEE802.1w-Rapid Spanning Tree Protoco IEEE802.1Q -VLAN Tagging IEEE802.1s Multiple Spanning Tree Protocol IEEE802.1p -Class of Service IEEE802.1X-Port Based Network Access Control GVRP/RIPv1/v2&OSPFv1/v2/v3/VRRP/DHCP/CLI/EAPS/Qos/LACP/LLDP/IGMP/PIM/SNMP/SNTP/SSH |
| Switch properties |
| Priority queue | 8 |
| VLAN ID | 4096 |
| IGMP Groups | 512 |
| MAC table | 16k |
| Switch Bandwidth | 56Gbps |
| Route Table | 8k |
| Switch Delay | <5μs |
| Interface |
| Gigabit ports | Port numbers: 28 |
|  | Connector: SFP for fiber port(LC, single or multi-mode), RJ45 for copper port |
|  | Baud rate: 1000Base-LX(fiber port), 10/100/1000M for copper port |
| Console port | RS232, RJ45 |
| Terminal block for power input | 5.08mm terminal block |
| Terminal block for relay alarm | 5.08mm terminal block, 1A@24VDC |
| Communication distance |
| Twisted-pair | 100m(CAT5/CAT5e cable) |
| Multimode fiber | Gigabit multi-mode: 850nm 550m |
| Single mode fiber | Gigabit single mode: 1310nm 20km |
| LED indicator lights |
| Front panel LED | Port light: LINK/ACT, SPEED |
|  | Running light: RUN |
|  | Power LED: PWR1, PWR2 |
|  | Alarm LED: Alarm |
| Rear panel LED | RJ45 LED: LINK/ACT, SPEED |
|  | Fiber LED: LINK/ACT |
| Power Requirements |
| Power input | AC/DC220V(85-264VAC/110-370VDC) |
| Full-load consumption | <27W |
| Overload protection | Support |
| Reverse protection | Support |
| Redundancy protection | Support |
| Working Environment |
| Operating Temperature | -40°C~70°C |
| Storage temperature | -40°C~85°C |
| Ambient Humidity | 5%~95%( non-condensing) |
| Physical Characteristics |
| Shell | IP40 protection, aluminum alloy shell |
| Installation | 19" 1U rack mounted for front and rear outlet installation |
| Dimension | 482.6 mmx44mmx315mm |
| Industry standard |
| EMC | EN61000-4-2(ESD),Level 4 EN61000-4-3(RS),Level 4 EN61000-4-4(EFT),Level 4 EN61000-4-5(Surge),Level 4 EN61000-4-6(CS),Level 4 EN61000-4-8,Level 5 |
| Impact | IEC60068–2-27 |
| Falling | IEC60068-2-32 |
| Shock | IEC60068-2-6 |
| Warranty |
| Warranty | 5 Years |
| Certification |
| Certification | CE, FCC, RoHS |

# Dimensional drawing

Rack mounting (Unit: mm)

| Ordering Information |
| --- |
| MISCOM8028G-8GC-4GF-16GT-AD220 | 8 Gigabit combo ports +4 Gigabit Fx ports +16 Gigabit Tx ports, layer 3 full Gigabit rack-mounted industrial Ethernet switch, single AC85-264V/ DC110~370V isolate power supply |